Solar Powered Car

| The chassis and electronics |
| --- |
| Wk1 | Discuss solar panels/positive/negative issues. Examine the ‘Glowstar’ light in detail. HWK: Ask students to research either wind power, solar power, water power or geothermal power and create a presentation to discuss with the rest of the class. Design 3 products that may be solar powered e.g. calculators, satellites, houses, cars, watches, PDM’s. Show example cars, discuss components. Show website http://www.riomay.com/ If possible watch Glowstar Video and Bio diesel video (must purchase video pack). Questions and answers. http://www.itdg.org/ Students produce Gantt Chart or flowchart of the next 5 weeks. |
| Wk 2 | Draw example of car chassis/circuit and label components. Write Specifications for solar powered car. Go through circuit-draw a circuit diagram using Crocodile clips and 3D pictorial diagram of circuit. Ask students to create circuit diagram using crocodile clips. Produce Orthographic drawing of chassis and pictorial drawing with sizes. |
| Wk3 | Cut out plywood base –start to make the chassis by: Marking out and cutting the slot for the pulley Cut lengths of bar for axles Cut lengths of MDF and use the drilling jig to drill holes for axles. Glue the MDF strips to the chassis |
| Wk 4 | Mark out and cut the slot for the sliding switch. Glue the switch into position. Attach wheels, pulley, axles and elastic band. Sand the chassis. |
| Wk5 | Demonstration on how to build the circuit and how to solder. Connect the motor wires from the motor to the switch. Glue the motor into place with the elastic band attached. Solder in the wires to the solar panel Connect the capacitor to the solar panel wires. Attach the solar panel, charge and test. Make improvements and adjustments |
| Wk 6 | Race and test the car over a short distance and place times into a chart. Write an evaluation of the process and thee success of the car. Make a diary of construction. |

| The Body of the car |
| --- |
| Wk 1 | Students use the internet to research car bodies. Produce Research sheet and add notes. Discuss aerodynamics and monocoque structures. Show photographs of solar powered cars. |
| Wk 2 | Demonstration of the use of: Corroflute CAD nets Card Acrylic Polypropylene Mounting board Aluminium Strip bender Vacuum forming 2D design and Camm 1 Line bending aluminium. Edge treatment of acrylic Use Manufacturing Plastics CD Rom and Focus on Plastics. Students produce 2 sheets of initial ideas using techniques demonstrated in this lesson. Graphic techniques, use of graphic media. Students produce instruction sheet on the use of vacuum forming for other students to use. |
| Wk 3 | Students choose 1 idea and develop it. Measure the chassis to collect correct sizes and look at working drawing they produced when making the chassis. Show how they intend to make the bodywork. Show/explain which materials they have chosen and give reasons for their choices. Show Birchfield Properties of Materials CD Rom and Woods, Metals, Plastics CD Rom. Explain where the solar panel will live and how the circuit will fit into the body. Explain how they intend to attach the body to the chassis and maintain the circuit. Produce a working drawing of the body shell by tracing the working drawing of the chassis and making a transparent overlay. |
| Wk 4 | Students chose their materials and begin to make their car bodies. Make templates. They will need to keep a diary of all practical work. Explain their quality control measures. |
| Wk 5 | Students complete the car body and add graphics using Camm1. Demonstration of the use of Camm 1 to cut vinyl lettering. Students attach the bodies to the chassis. Reattach the solar panel to the top of the car. Test the cars again and record times. Students produce instructions sheet on the use of Camm 1 |
| Wk 6 | Complete the car and evaluate. Use Key Stage 3 Strategy (design and evaluation activities). Exploded drawing of car. |